## Slide 1
PAS cell
Flow Controller
Flow Controller
Vacuum Pump
Acoustic Filter
Single Channel CRD-PAS Flow Diagram
Flow Controller
Filter
Scrubber
Vent
Drier
Impactor
Inlet
Four way crossover valve – aerosol compatible
Purafil Scrubber
Filter
Flow Controller
O3 lamp
Mirror Purges
Critical-O in each line
Counter flow
through drier
Compressor
The compressor pulls from the exhaust because this is dry air and free of NO2 and O3.
100 sccm
40 ccm
Vary lamp power or flow to adjust O3 concentration
1 lpm
1-3 lpm
1-3 lpm
3-7 lpm
Critical-O: keeps O3 gen. at constant pressure
Up to 500 ppm O3
SS Valve must withstand 500 ppm O3
Cycling:
State 1 - Sample: The PAS cell and CRD cell 2 measure aerosol. CRD cell 1 cycles between gas phase extinction and filtered sample air.
State 2 – Filter: The PAS cell and CRD cell 2 measure filtered air. CRD cell 1 measures aerosol.
State 3 – Speaker calibration .
State 3 – O3 calibration.
State 4 – Q pressure measurement.
State 5 – O3 pressure calibration.
Solenoid valve
No aerosol trans
Solenoid valve
No aerosol trans
Solenoid valve No aerosol trans
Manual 3-way valve
Possibly only connected to supply power
Reynolds numbers (1 atm and 20 deg C)
5/32” ID tube
5 lpm – 1808
7 lpm – 2532
10 lpm – 3617
3/16” ID tube
5 lpm – 1570
7lpm - 2198
Transition regime for tube flow
2300 < Re < 4000
Flow Controller
Filter
Purafil Scrubber
Pressure
Pressure
Pressure
CRD cell 1
CRD cell 2
Optical and Acoustic box
Vacuum Pump
Pressure Controller
Inlet pressure control:
Only needed on aircraft
Maybe on the BAO tower.
TD/RH